INSTALLATION MANUAL

### Client setup
To setup the device, place it at the desired location.
Plug in the USB cable into the device as pictured below:

### Server setup
Plug in the other end of the USB cable into the device that should run the server:
Test and make sure the server device is connected to the internet.

### Software compilation
- To compile the software, you will need the following tools:
- Terminal/command prompt – Operating systems usually have this pre-installed
- GNU make/MinGW - https://sourceforge.net/projects/mingw/
- Arduino IDE - https://www.arduino.cc/en/main/software
Once downloaded and installed, run Arduino IDE and open client.ino inside the client subdirectory from the source code’s root directory. Make sure “Arduino/Genuino Uno” is selected in Tools > Board and Tools > Port has the correct port selected in which the client device is connected:

Now press upload:

When the client has uploaded successfully, open a terminal/command prompt and navigate to the source code’s root directory.
From here navigate to the server subdirectory.
Run make command:
Once completed, you can now start the server by either using make run command:
Or just run it directly: ./bin/gad.exe:

### Configuration
The server needs to have users configured. These can be defined in the users.dat file in server	root directory. The format of a user should be written in a CSV format	(https://en.wikipedia.org/wiki/Comma-separated_values)
The table below describes each field:
userID;pincode;username;tagID;status;reserved
userID	ID of the user (digits only)
pincode	PIN code of the user (4-6 digits)
username	Name or alias of the user (letters only, A-Z, upper or lowercase)
tagID	The ID of the user’s tag, if the user has one, otherwise specify -1 (digits only)
status	Current user status: / 1 – User is active and can log in anytime / 2 – User is currently inactive and is unable to log in / 3 – User is blocked and is unable to log in
reserved	Not a currently used field, this can be ignored

Examples:
1;KalleAnka;1234;101;1;
2;AlexanderLukas;03459;-1;3;
5;JoakimVonAnka;985230;105;2;

NOTE: By default, the root user is present and active with the PIN code 0000.
This code should be changed as soon as possible.
### Logging
There is two types of log files located in the server root directory.

First one is named system.log and has CSV (see configuration) values of users interacting with	the alarm central. The file has the following layout:
index;date;userID;reserved;message
index	The log entry index
date	Time and date of the event
userID	ID of the interacting user. This field has a value of -1 if the user cannot be determined (For example: If the user typed the wrong PIN code)
reserved	Not a currently used field, this can be ignored
message	A message text describing the type of event

Examples:
0;1970.01.01 00:00:00;0;;User login successful
1;2018.12.24 01:15:32;3;;Alarm activated to mode A
2;2019.01.06 16:20:42;-1;;Failed login attempt

There is also a sensor status file for writing/reading current sensor statuses. This file is names	sensors.dat and is automatically updated whenever a status changes and holds ID and Status	fields described below:
ID;status
ID	ID of the sensor
status	Current status / 0 – Sensor is closed/not triggered / 1 – Sensor is open/triggered / 2 – Sensor registered a malfunction and may need maintenance

### Sensors
There’s two types of sensors: Magnetic switches and sonic motion sensor.
Magentic switches should, for example be installed on doors and windows or any other opeanable/breakable entry point to the protected area. They should be placed close enough to each other to make contact. When the sensors are active and lose contact with one another, the alarm will trigger.
Motion sensors should preferably be placed aloft, facing a plain surface, wall or door of what would be a possible entry point for a trespasser. Having several object with different distances form each other in front of the sensor may trigger a false positive alarm. When motion sensor is activated, it scans the distance to the target surface and keeps that value for future comparisons. Whenever the distance is changed i.e. something has moved in-between the sensor and the surface, the alarm will trigger. Therefore, be cautious to have moving entities in the area as this sensor is activated. The motion sensor has a distance threshold of 0.5 meters (1.64 ft). If the motion sensor would break from a defect or a distance read failure due to getting the initial monitoring distance at activation process, the alarm will also trigger. This will happen if the duration of faulty readings reaches 1 second and above (5 seconds at the startup process).
### Circuit diagram

### Breadboard schematic